## Slide 1
CONTROLLED BY: U.S. NAVY, STRATEGIC SYSTEMS PROGRAMS CONTROLLED BY: SP23 FIRE CONTROL AND GUIDANCE BRANCH CUI CATEGORY: CTI, Proprietary Information DISTRIBUTION/DISSEMINATION CONTROL: DISTRIBUTION STATEMENT D POC: Matthew Jamula, mjamula@draper.com WARNING: THIS DOCUMENT CONTAINS TECHNICAL DATA WHOSE EXPORT IS RESTRICTED BY THE ARMS EXPORT CONTROL ACT (TITLE 22, U.S.C., SEC 2751, ET SEQ.) OR THE EXPORT ADMINISTRATION ACT OF 1979 (TITLE 50, U.S.C., APP. 2401, ET SEQ.), AS AMENDED. VIOLATIONS OF THESE EXPORT LAWS ARE SUBJECT TO SEVERE CRIMINAL PENALTIES. DISSEMINATE IN ACCORDANCE WITH PROVISIONS OF DOD DIRECTIVE 5230.25. DISTRIBUTION STATEMENT D: DISTRIBUTION STATEMENT D: DISTRIBUTION AUTHORIZED TO THE DEPARTMENT OF DEFENSE AND U.S. DEPARTMENT OF DEFENSE CONTRACTORS ONLY. ADMINISRATIVE OR OPERATIONAL USE 19 May 2022. OTHER REQUESTS SHALL BE REFERRED TO DIRECTOR, STRATEGIC SYSTEMS PROGRAMS. DESTRUCTION NOTICE: DESTROY BY ANY METHOD THAT WILL PREVENT DISCLOSURE OF CONTENTS OR RECONSTRUCTION OF THE DOCUMENT. THIS PRESENTATION CONTAINS DRAPER PROPRIETARY INFORMATION.
ERB Communications Task
10/2/2023
Andrew Stone

## Slide 2: Comms Approach
Provide deterministic and testable communication for guidance and avionics domains that scales with SWS LE2 requirements and future enhancements

## Slide 3: High Level Internal Comms Summary
Alternative approaches based on SSDN gaps:
  Gaps with flexibility, VSSIM, preplanned slot timing, throughput, reduced IO slip ring count
Increase test capability, concurrent test analysis with tactical timeline
Increase built-in-test capability
The reason we looked at serial bus technologies is because of slip ring count
Analyzed industry standard protocols: MAC-level switched topology still a possible candidate
Take advantage of todays technology with respect to physical layer and increased processing

## Slide 4: SSDN Mod1 Selection and LE2 Architectural Deltas
What Drove the SSDN Selection on Mod1?
  Started off with higher voltage logic levels in Mod0
    Wanted a step change to lower voltage drivers/receivers
    Ethernet wasn’t mature at the time. Ethernet was a CSMA/CD design
  Needed a rad hard solution that had fast recovery
  Strict timing and determinism for the instrument control loops
  Limited processing power with multiple distributed single processors
What are the architectural deltas associated LE2?
  Processors with orders of magnitude more processing power
  Processor chips with multiple cores eliminating the need for multiple distributed single processors
  Improvements in high speed SERDES communications including Ethernet
  Full duplex deterministic switching topologies with single microsecond latencies
  Improvements in driver and receiver technology. Lower SWAP components. Improved edge rates, latencies

## Slide 5: Internal Comms Approach
Analyzed existing SSDN for improvements
  Greater data flexibility to mitigate SSDN slot rigidity
  Reduce software and hardware timing dependencies for data scheduling and computations
  Adding full duplex communication
  Improving overall bandwidth.
  Reduce IO count for slip rings and for cabling
  Improve built-in-test
  Simplify HWIL and VSSIM slot rigidity and long simulation time due to 2 microseconds slot time
  Reduce size, weight and power.
  Remove need to preplan slot assignments
Investigated:
  Increased need for stellar bandwidth. Interleave stellar with data or provide a separate channel
  Timestamp intrinsic to IMU data at point of generation
  Fiber vs copper internal – Fiber had larger SWAP footprint
  MAC-level switched topology
  Possible internal topologies:
    Multiple point-to-point internal links
    Like LE1 with Middle Gimbal Electronics
    Electronics on all Gimbals
    Processor in Case Mounted Electronics (CME)
    Multiple processors. Processor in CME, processor in MAP/EA
The Details Following will examine a Full Duplex Hybrid Approach that attempts to improve upon the previous design

## Slide 6: Lessons Learned from LE
Continued tactical focus with increased focus on test
  Allow real-time system feedback and visibility (continuous monitoring and triggering)
  Continued and improved focus on HWIL and VSSIM modeling and simulation
Requirement to use general guidance bandwidth for Stellar creates bandwidth restrictions.
Multiple pt2pt interfaces (SSDN, Fire Control, Missile/Flight Control/AMP/TLM/etc) makes test equipment development timely and costly
Reducing custom interfaces to reduce test equipment cost and development time
  More emphasis on open standards vs custom hardware
Existence of incompatible data input and logging formats for test tools duplicates effort and complicates development of test tools
Provide capability going forward for capturing all data from any external port (testport and avionics (FC) port)
Reduce complexity of re-configuration of SSDN data for future enhancements

## Slide 7: Throughput Analysis - Camera
Comms system should support 1.5x the required throughput to account for processing delays and transmitting/receiving data via DMAs or other means to keep up with 50 frame/sec rate
 | SSS sensor full frame | Bits/ pixel | Bits/ frame | SSS ASIC input frame capture rate (raw data) | SSS ASIC memory to store 10 frames of data | SSS ASIC output frame rate (processed data) | SSS stellar payload data bits/ sec | 8B/10B Overhead | Comms stellar data rate
LE2 | 150 x 150 pixels | 12 or 14 | 315,000 | High-Speed sensor 1ms or 1000 frames/ s | 14 bits/ pixel need 2.7 Mbits of memory to store 10 frames of image data | High-Speed sensor 20ms or 50 frames/ s | 31,500,000 | x1.25 | 39.375mbps
 |  |  |  | 5ms or 200 frames/ s |  | low-Speed sensor 50ms or 20 frames/ s | 5,400,000 | 7,200,000 | 9.36mbps

## Slide 8: Requirements
Requirements have been captured for the guidance internal network, mission critical network, high bandwidth network, and TLM network.
Network_Requirements.xlsx

## Slide 9: Guidance Internal Network Options Considered
Option | Pros | Cons
Ethernet | COTs solution with common industry use | Requires processor at all nodes.
Min Config TDMA – Half duplex | Added flexibility. Flexible frame/slot configuration Expandable to mission network. | Additional time required for network configuration. Network controller needs logic and access to message dictionary. If used for Mission Network, full SWS timeline not known until full system is configured.
Full Duplex TDMA Stack-Based Design | Added flexibility. Messages added to Tx FIFO when sampled data updates are complete. Expandable to mission network | If used for Mission Network, full SWS timeline not known until full system is configured. Wiring needs to prevent Tx contention (no issue if pt2pt) Full duplex could add complexity on test port if IMU downstream gimbal-gimbal comms are added in LE2
SSDN | Proven Expandable to mission network Predictable, coordinated message dictionary | Pre-programmed message dictionary Limited flexibility, but could be updated to improve

## Slide 10: High Bandwidth Network Options Considered
Option | Pros | Cons
Existing Legacy Design | Existing design. Proven at low data rates. | Cannot meet high bandwidth needs
Existing Umbilical Updated with RS422 drivers and multiple parallel wires to get desired bandwidth | No updates to umbilical. Use 10 available umbilical spare wire pairs Can achieve bandwidth between 100Mbps-200Mbps using parallel network design. | No additional bandwidth flexibility unless pins are added to umbilical.
Copper-based Ethernet | Added flexibility with COTs approach Move towards cabling with better impedance control | Network bandwidth still severely limited by copper interconnect and interfaces May not meet desired bandwidth
Fiber Ethernet | Significant bandwidth increase Flexible margin for future needs Comms network will not limit pre-launch timeline Lower weight Reduced SGEMP requirements | Requires novel (potentially costly) umbilical update

## Slide 11: Internal Comms - SSDN
Half duplex, shared bus.
Time synchronization is done by putting messages into slots and frames at specific times.
  Slots make the system very rigid.
Stellar Camera intermingled with data. Camera data in original system ~1/3 of total data
Asynchronous messages needed at beginning of C&R to recover reprogramming of system
Changing message size or placement is a complex puzzle. For example, imagine making message 96 larger.
All messages on bus regardless of destination
Testing limited to pre-defined messages with pre-defined functions. Difficulty to add in messages later.
Throughput of current system limited by choice of drivers, transformers and cabling to EA. This can be updated going forward
Uses HB/LB dual channels in each direction. Could be simplified to 1 channel in each direction
VSSIM modeling extremely difficult and causes long duration sims
“SSDN is like dried concrete that you need a jackhammer to remove” – VSSIM Developer

## Slide 12: Internal Comms -Full Duplex Hybrid Approach
Full Duplex Hybrid Approach
  Sensor data captured on frame and clock offset timing mark – Gimbals, IFOG, PIGA
  As deterministic as SSDN is. No need to preplan slots and have a complex ICD
  Flexibility:
    Greater flexibility for VSSIM and HWIL
    Using a small percentage of the bandwidth. Full Duplex frees up more bandwidth
    Change the size of messages without having to update the communication HDL and slot allocation
    No longer have to pre-schedule slots
  Carries forward: 8B/10B encoding, Rad Hardness, C&R fast recovery, Test Port to echo internal data, Frame Timing, Common HDL blocks, Common Driver/Receiver circuitry
  Eliminates extra wires needed for Sync by using clever 10bit encoding
  Eliminates extra wires needed for GIE/Break by using clever 10bit encoding
  Eliminates need for slot timing and complex software/hardware timing dependencies
  Data priority scheduling is based on pre-emptive OS, and not on when a particular slot assignment is destined to arrive.
  Would use a DMA to transfer data direct to memory for microprocessors
  Adds full duplex communication
  Improves bandwidth via new physical layer
  Add Built In Test (BIT) PRBS generator/checker

## Slide 13: Full Duplex Hybrid Approach
Provide a flexible architecture that can adapt to various rate traffic and placement of electronics
Common HDL across all regions
All instrument Data latched on programable hardware timing mark – Gimbals, Accelerometers, Gyros.
  TBD storing of hardware sampling timing mark for gimbal electronics if no NVRAM present.
Uses 3 sets of slip rings including a dedicated stellar channel. Includes encoded GIE/Break, Sync. Current LE: 6 sets of slip rings
No risk for HDL approach.
Physical layer requires collaboration with Electronic Parts Working Group (EPWG). No risk. Only risk is if we fall back on existing drivers/receivers. Existing drivers/receivers may not support Stellar BW. Existing drivers/receivers will not support digital clock.

## Slide 14: Timing For Link A
Messages are received by all electronics like a broadcast via a pseudo multi-drop arrangement
Depending on origin of message (CME vs MAP/IAP) FIFO at CME could provide arbitration
At the 100Hz timeline with 23mbps this provides:
  12% of utilization at 100Hz, <1% utilization at other 600Hz
Flexible time could be used for Test or Debug (Command/Response)
Tactical Messages Sent to Gimbals or Stable Member | 16-Bit Words
msg_MSS_EA_100HZ_MODE_MET | 21
msg_MSS_EA_100HZ_SUBSYS_CMDS | 75
msg_PCSS_300HZ_HTR_CMDS | 4
msg_SSS_EA_20HZ_SSS_SM_DATA | 185
msg_SyncPulseMsg | 10
6 600Hz Frames

## Slide 15: Data on Link B
6 600Hz Frames
Tactical Messages | Size in 16 bit words
msg_AMSS_SM_100HZ_GYRO_DATA_FOR_MSS | 31
msg_VSS_SM_100HZ_ACCEL_DATA_FOR_MSS | 43
msg_OG_600HZ_RESOLVER_DATA | 40
msg_MG_600HZ_RESOLVER_DATA | 40
msg_IG_600HZ_RESOLVER_DATA | 40
msg_SG_600HZ_RESOLVER_DATA | 40
msg_AMSS_SM_300HZ_GYRO_DATA_FOR_PLAT_CTRL | 7
Diag Messages | 
msg_VSS_SM_100HZ_RFT_SWM_DIAG_DATA | 133
msg_SSS_SM_20HZ_RFT_DIAG_DATA | 53
msg_AMSS_SM_100HZ_RFT_SWM_DIAG_DATA | 123
msg_OG_100HZ_RFT_DIAG_DATA | 100
msg_MG_100HZ_RFT_DIAG_DATA | 100
msg_IG_100HZ_RFT_DIAG_DATA | 100
msg_SG_100HZ_RFT_DIAG_DATA | 100
TOTAL | 950

## Slide 16: Timing For Link B
Table above assumes instrument traffic sent at rate listed. See timing diagram
Messages are sent from SM down to Gimbals. FIFOs buffers up whole messages and logic decides whether to send local data or data in received FIFO.
Straightforward HDL logic
Internal FIFO to FIFO transfer rate runs at 4x line rate for minimal latency. FIFO size could be double the worst case to account for future growth
Flexible time could be used for Test or Debug (Command/Response) or the Stellar Channel could be used to return data
This approach provides flexibility to run at any rate with margin
6 600Hz Frames
 | 23mbps Typical@600Hz | 23mbps @2400Hz | 96mbps @600Hz | 96mbps @2400Hz
Transmit Time us | 297 | 297 | 71 | 71
FIFO Time us | 74.25 | 74.25 | 17.75 | 17.75
Total Time | 371.25 | 371.25 | 88.75 | 88.75
Percent Utilization | 371.25/1666 =22% | 371.25/416 =89.2% | 88.75/1666 =5% | 88.75/416 =21%

## Slide 17: Built-In-Test (BIT) PRBS Block Diagram
PRBS demo circuit designed using the Xilinx ZCU102 FPGA
User interface designed to start and stop PRBS output and check for communication errors

## Slide 18: Internal Comms Takeaways and Status
Takeaways
  SSDN shortfalls are mitigated by Full Duplex Hybrid Approach
  Flexibility for expansion with test
  Approach based on today's technology
  Built-in-test from the get-go
  Integrates discretes such as sync and gie/break into comms
Status
  Currently have 3 physical layer boards ready to be built to test physical layer for margins as well as an entire simulation of all guidance traffic.
  HDL already developed to test all internal traffic
  Have a method to inject noise into system while running built-in-test and/or real guidance traffic models
  Have fully functional discrete and sync injection into system
  Have fully characterized current slip rings. Measured S-parameter model was used to vet physical layer designs for margin

## Slide 19: Physical Layer

## Slide 20: Advantages of LVDS-like Communications
Next slides presents only differential communications physical layer options
MLVDS/LVDS offers superior data rate, lower power consumption, and lower EMI emissions than RS422 while being tolerant to large common mode noise (especially in space rad-hard receivers).
Most modern LVDS drivers now have a failsafe built-in feature which sets the output to ‘high’ when input is high-z. This is needed for AC coupled/transformer coupled solutions.
Reduction in power supply noise compared to single ended since output current remains constant. Less need for power supply decouplers
LVDS/MLVDS or LVPECL/CML are the leading contenders
LVPECL and CML offer a larger output swing voltage. Results in lower jitter, but higher power consumption. May offer improved EMI susceptibility.

## Slide 21: Internal Comms Physical Layer Standards Evaluated
Standard | Power (mW) (single channel) | Data rate (Mbps) | Voltage Output Swing min (mV) | Rx Input Threshold (mV) | Common Mode Input Range (V) | Skew (ns)/ Propagation Delay(ns) | Features | Complexity
RS422 | 100 | 30 | 2000 | N/A (LVDS rx) | N/A (LVDS rx) | 10/70 |  | 8b10b
MLT-3 | 200 | 100 | 2000 1V per symbol | 200 |  | 200ns | Reduced BW | Voltage encoding + 4b5b or 8b10b
LVDS | 45 @ 100 MHz | 400 | 250 | 50 *commercial go lower | -4 to 5 | 0.6/4.5 | Failsafe Bias | 8b10b
MLVDS | 17mA | <200 | 480 | 50 *commercial go to 35 | -1.4 to 3.8 | .6/10 | Detects open circuit for failsafe | *could not find any space rad hard *use as pt-pt
CML | 180 | >1000 | 650 | 200 | 1.5 to 2.4 | 0.1/1 |  | 8b10b
LVPECL | 82 | >1000 | 1100 | 200 | 2 to 3.2 | 0.05/.45 |  | 8b10b

## Slide 22: Internal Comms System Requirements
Future enhancements in compressed schedule
Enhanced data logging with test equipment
Timing:
  CTTS to generate and distribute Ref_Clk to all GS modules, within 100 us after release of PFI with less than 1 ns cy-cy RMS Jitter
  REF_CLK tunable oscillator will be locked to Fire Control timing during prelaunch and held during flight with TBD ppm accuracy
  Internally generated Sync is synchronized with Nav 1PPS
  GS modules to receive Sync with less than 200ns of skew and less than 200ns p-p jitter
Sampling:
  Subsystems will receive timing information for instrument sampling
    Less than 200ns of Sync Pulse skew in all regions
  Sampling of the instruments needs to be on the same time mark every time
    Resolvers and Gyros need to be sampled on the same time mark within 5us (TBD)
  Torque motor commands/direct torque needs to be sent on the same time mark every time

## Slide 23: Internal Comms System Requirements Cont’d
Recovery:
  Transmit reference clock and any needed discretes as soon as power is stable to allow IMU ASICS to start sampling instruments and generate data to transmit on comms infrastructure
  Manage and synchronize the release of PFI (System Reset) to all subsystems
  Meet similar LE ~2.5ms circumvention and recovery timeline. 3-7ms for flight control
Slip Ring and wiring Spec’d out for controlled impedance and return/insertion loss similar to IEEE 802.3 100BaseTX spec
Every message sent in the system is recorded. This can include inter processor core messages.
Support a Bit Error Rate for error free comms within a TBD hour period of time in the presence of an additive white Gaussian noise distributed over a bandwidth of 1.0 kHz to TBD MHz at a RMS amplitude of 140 mV
  Derived into jitter requirements
  Needs additional assessment
Maintain galvanic isolation between guidance regions
SGEMP transients, per OD 64856 in cases where the Subsystem has a direct connection to any of the following external connectors

## Slide 24: Avionics Network

## Slide 25: Managed Systems Communication Approach
Established a systems approach to the network design (Physical Interface to Application)
  Fully characterized communications for current and future enhancements
  Complete understanding of all data paths and requirements
Established HW/SW element capabilities and characteristics
  Software/Hardware latency, BW, timelines, timing and synchronization
  Understood network environment/topology/data paths that are static
Established a common API for all software developers to access the communication bus:
  Software developers shouldn’t need to know or need to understand the systems approach to the network design
  Common API locks down features such that the network is predictable and reliable.
Real-Time monitoring of network configuration and status/errors
Future expansion
  Predictable system margins throughout D5-LE program with new network node reallocation or new network node additions
Command Response for real-time test and diagnostics
  Test integrated with internal comms timelines

## Slide 26: High Level Avionics Comms Trade Summary
Review of industry standard protocols:
  Ethernet and supporting protocols on top of Ethernet – DDS, LCM, Time Sensitive Networking, SNMP, ARINC 664
  SpaceFibre
  Point to point protocols like: Aurora, interlaken
  Other protocols quickly ruled out: CAN, 1553, EtherCat, Time Triggered Ethernet (TTE)
Analysis of optics based physical layer vs copper
  Ongoing trade on copper technologies
  Very thorough trade almost complete on fiber optics technology
All protocols and physical layers examined for Trident specific requirements:
  Strategic Rad Hard
  Startup Timelines
  Mechanical and environmental
Recommendation is: Switched Ethernet over integrated fiber optic transceivers to support both high speed and real time communications
SSDN on Avionics network is not flexible, scalable and very difficult to use
Ethernet Approach will be fully characterized from API to API

## Slide 27: Fiber Optics Trade Study
Fiber optics offers clear advantage over copper for the following reasons:
  Immune to electromagnetic interference and does not generate EMI
  Long distances up to 550 meters
  Radiation hardness of fiber optic cabling
All components evaluated for the following criteria:
  Mechanical shock/vibe
  Radiation Hardness
  Circumvention and Recovery Time
  Auto test/ monitoring capability
  Optical link budget, power consumption, data rate, commercial maturity
Evaluated transceivers:
  Includes VCSEL or other laser drivers
Evaluated fiber optic cabling
  Evaluated multimode vs singlemode. APC vs UPC
Evaluated fiber optic connectors
  Evaluated backplane connectors
  Evaluated high insertion military connectors

## Slide 28: Fiber Optics Summary/Recommendations
Transceivers:
  Samtec FireHawk or Smiths SpaceABLE are built on a radiation hardened process technology
    Samtec FireHawk extensively tested in the lab. Ran for 2.5 days at 1gigabit with 0 errors. Optical tests pass all IEEE standards with ample margins
    Samtec FireHawk process technology reviewed by Steve Hoeschele and says it is a good candidate.
  Both include VCSELs, which are the most desirable for radiation hardness (details in report)
Fiber optics
Name | Vendor | Radiation induced attenuation -RIA (db/100m) | Fiber Type | Commercial Maturity | Core Attenuation (db/Km)
Super RadHard | Prysmian Group | 4.7@ 850nm*** 2.2@ 1300nm | MMF |  | 2.6@850nm 0.6@1300nm
Model | Vendor | Rad | Vib | Circumvention Time | Commercial Maturity | Form Factor | Optical Specs | Data Rate | Power Monitoring
FireHawk | Samtec |  |  | <1.2ms |  | Quad XCVRPCB Mount | 850, MMF | 1/10Gbps | Yes, SPI

## Slide 29: Fiber Optics Summary - Connectors
Fiber Optic Backplane Connectors
  Use VITA 66.4 or similar
High Insertion Count Connectors:
  Use GlenAir Eye Beam GLT.
  Expanded Beam with alignment
Low Insertion loss Connectors:
  38999 connectors with ceramic ferrules

## Slide 30: LE2 PDU External Comms Objectives
Support existing LE requirements
Support systems integration with hardware in the loop
Support new CONOPS
  Fire Control to RB Prelaunch – Allows for shipboard prelaunch initialization
  In Flight Guidance RB alignment – continuous ~100Hz data between Guidance and RBs
  Timing/Timeline Sequencing/Control
  Large data file transfers to RBs, without affecting real-time communication
  Missile-to-Missile direct comms
  Receipt of full 16Hz Nav Data
  Logging of guidance and avionics subsystems data. Cloud storage/analysis?
System Support and Deploy future enhancements with REDUCED schedules:
  Modularity, commonality, enhanced test, cyber mitigation
  Data Adaptability to handle new RBs and internal guidance changes
  Improved testability and continuous monitoring
  Use logged/real-time data to rapidly assess failures, health, welfare and performance of the system
  Future Mission Applications

## Slide 31: LE2 Expected Ethernet Recovery Timeline
50 us
105 us
185 us
285 us
3 ms
4.03 ms
0s: Processor reset is released; recovery begins.
50 us: Security Engine completes Fast Boot; Omaha cores enter Recovery Init state
105 us: Recovery Init state completes; Mission early recovery & ethernet stack init begin in parallel.
185 us: Configuration of PHY layer complete
200 us: MSS Early Recovery complete (estimated)
285 us: Configuration of Omaha internal registers and memory complete. Programming of Fiber XCVR
1.4 ms: Fiber optic transceiver operational
3 ms: Required minimum delay after release of reset for completion of MDB transmission to FCEA
4.03 ms: MOD 1 observed time after release of reset for internal transmission of MDB from MSS to IOSS
7 ms: Required maximum delay after release of reset for completion of MDB transmission to FCEA;
Mission hardened object repair completed.
8.5 ms: MSS recovery complete (not shown on timeline)
7 ms
-1 ms 0 ms 1 ms 2 ms 3 ms 4 ms 5 ms 6 ms 7 ms
200 us

## Slide 32: Fast Boot & Ethernet Stack
Reconfiguring network after reset using saved configuration requires writing a few dozen regs on GRadSoC processor & PHY chip
  Exact number depends on PHY chip selected.
  PHY chip connected by 10MHz SMMI bus; est time for 50 16-bit regs: 80 us
Message stack can be tweaked for a zero-copy approach
  Eliminates need for final copy on Ethernet
Total boot time for an ethernet stack in recovery is expected in the low 100s of us & can be done in parallel w/ Mission startup & MDB generation

## Slide 33: Avionics Network
Spare Ports on Switch for future payloads

## Slide 34: Timing and Determinism of ENET
Mission Network Is Not Needed
  Ethernet approach supports both file transfers to RBs and real-time comms
  Single packet exceeds the current interface for latency
From an Application to Applications viewpoint there are 4 areas of arbitration and management:
  Scheduling priority of tasks
    Optimize the task priorities
    Possible - assigning single core to IOSS functionality
  Single microsecond latencies through a layer 2 switch
    Does not use IP switching, only MAC level switching
  Streamlining the stack code
    Optimize the stack code configuration
    Managing a Queue of messages
    Encapsulating data into a single message – no queuing in switch
  Common API(s) that are shared amongst contractors
Characterization of Application to Application (AP2AP)
  Scalability and Flexibility
    All Current Conops will be fully characterized and allows for future margins and future conops
    To introduce new Conops the only modification required is to the API
  Physical layer, stack, network switch latencies will be fully characterized

## Slide 35: ENET Timing Diagram – Fire Control

## Slide 36: ENET Timing Diagram – 100Hz Avionics

## Slide 37: ENET Timing Diagram – Internal Guidance Echoed to Avionics ENET
Built-in Comm Emulator
All data contains frame numbers and 64bit time tags

## Slide 38: Middleware Tactical Data Flow Diagram
Missile Internals
Guidance
System
Flight Control
TLM
Interface
Reentry
Bodies
Fire
Control
Data
Recorder
Middleware Data Bus
Nav Data
GS/FC Comms
RB Comms
Diag Data
TLM Data
GS/FCEA Comms
Timing Discretes

## Slide 39: Data Logging/display
Guidance system itself would become like a comm emulator giving you direct visibility into system over a user friendly ethernet interface.
A laptop could be connected for data logging or data display to test port or to avionics port. Laptop could be used to drive testing.
Timestamping could be intrinsic to internal IMU data at the source
Data generated on the internal bus would be bundled and echoed out of the test port/avionics port
With middleware technology, simply subscribe to data stream for internal IMU comms, or become a publisher of test data destined for internal IMU

## Slide 40: Coordinated Interface and Data
Application Layer
  Common Coordinated API across Avionics Network and Shipboard
Middleware Layer
  SWS Priority based traffic manager, data dictionaries
  Timeline management, Data logging, Data Visibility, Test Hooks
Transport, Network, Link
  Testing and profiling of MAC/PHY hardware layer
  Testing and profiling software stack implementation of Network Layer
Physical Layer
  Testing and characterization of physical layer
  Bit Error Rate (BER) and SERDES link compliance

## Slide 41: Test and Integration
Common middleware API to support tactical data as well as test data
Common network & COTS interfaces greatly reduces cost of test equipment development
Increased bandwidth margins allow collection of all SWS data and future payloads
Support common data logging format and virtual environment playback
Real-Time Health monitoring of system for out of spec or trending out of spec
Support integration test problems/failures at SWS level
Potential cloud storage of all data collected for current and future investigations

## Slide 42: SWS MBE Virtual Environment Simulation
Expansion of current Guidance virtual environment to include avionics subsystems and shipboard:
  SWS Avionics C&R verification and test
  Full Nav Data, RB alignment simulation and status, Flight Control simulation
  Distributed development & early integration between locations
Tactical
Playback Data
Network Switch
RB
Simulation

## Slide 43: More Backup

## Slide 44: Internal Comms Physical Layer Overview
Took measurements of existing slip rings with VNA to use for modeling
Simulated internal comms physical layers with LE slip rings and transformers.
Created a test bench to test candidate physical technologies with existing LE slip rings
Evaluated several physical layer technologies and will continue to evaluate
Working on several FPGA Mezzanine Card (FMC) designs to stress test comms system for long periods of time and with additive noise
Created Pseudo Random Bit Sequence (PRBS) -> 8B10B HDL generation and checker for running above bulleted point. Can then apply noise to this environment with current clamps.
Added special control characters into the data stream to test extraction of SYNC from data
Developing the HDL for a new comms system. Currently working on block diagrams for concept.

## Slide 45: RS422 Modeling - Mentor AMSVX2.8 using MOD_5672982 and MOD_5672983
MOD_5672983
MOD_5672982

## Slide 47: Hyperlynx Circuit LVDS TX and LVDS RX
There are 4 slipring models used in this circuit that are modeled using touchstone files created from measured sliprings
The signals are AC coupled using capacitors and biased using the voltage divider on the right
The driver is the ST-Micro RHLVDS315 and the receiver is the ST-Micro RHLVDS325 which are both tested to space radiation standards
The top circuit includes xfmr coupling while the bottom doesn’t

## Slide 48: Hyperlynx Simulation
The eye diagram is run at 100Mbps using PRBS-7 with 8b10b encoding
Pink is with transformer coupling and green is without
The transformer coupling closes the eye slightly and adds some delay
Transformer used is lower BW model up to only 200MHz
Currently measuring new transformer model that goes to 375MHz

## Slide 49: Physical Layer FMC Design
Designed with the Internal Comms High Level Concept 1 in mind
Schematic complete. Moving on to LRR. Working on alternate design with LVPECL.
FMC will be used to test the limitations of LVDS through the existing slip rings as well as xfmr and capacitor AC coupling
Three channels for passing data (PRBS with 8b10b) and one for passing the clock
Uses a source synchronous 150Mhz clock which is divisible by 2400Hz (existing rate)
  Clock can be divided in FPGA
Ability to bypass xfmr with jumpers evaluate the need for xfmr AC coupling
LVDS Chips use a common pinout/footprint so many parts can be tested on the same board
Ability to bypass the FPGA with jumpers to simulate data moving through multiple regions with a redrive
LVDS chips can be powered at voltage minimums for margin analysis
Alternate transmission protocol being evaluated :
LVPECL – has a larger differential amplitude swing than LVDS increasing the slew rate at the receiver and lowering the jitter

## Slide 50: Using Control Symbols to Create Sync
Control Symbols are 10-bit special characters that do not have a corresponding 8-bit character.
They are unique and can be used for low level control functions as shown below.

## Slide 51: PRBS Sync Insertion and PRBS Checker
PRBS provides large dataset to stress system and test all data points
Control Symbols (K.XX.Z) sent at rising/falling edge of 2400 clock
PRBS data and special characters are sent through the same wire
Sync Pulse Detector, detects control symbols and removes it from data stream while triggering clock edge switch
PRBS Checker ensures the data was received correctly

## Slide 52: Rotary Joint assembly - 2 Slipring in the Loop
Equivalent of 4 slip rings made from 2

## Slide 53: Experimental Set up to evaluate LVDS receiver
Initial evaluation, will use FMC board once completed

## Slide 54: Typical results obtained with a 100 Mb/s 8b/10b PRBS7 encoded pattern on without slipring assembly
Eye Jitter (RMS):12.84 ps

## Slide 55: Typical results obtained with a 100 Mb/s 8b/10b PRBS7 encoded pattern through 4 slip rings
Eye Jitter (RMS):16.81 ps

## Slide 56: Results obtained with an 100 Mb/s with 4 slip rings with added jitter 0.05RJ pp
Eye Jitter (RMS):43.51 ps

## Slide 57: Typical results obtained with 100 Mb/s 8b/10b PRBS7 encoded pattern on without slipring assembly
Eye Jitter (RMS):12.84 ps
Eye Jitter (RMS):29.31 ps
With Transformer
No Transformer

## Slide 58: Typical results obtained with an 100 Mb/s 8b/10b PRBS7 encoded pattern with 4 slip rings
Eye Jitter (RMS):16.81 ps
No Transformer
With Transformer
Eye Jitter (RMS):34.4 ps

## Slide 59: Results obtained with a 130 Mb/s 8b/10b PRBS7 encoded pattern with and without 4 slip rings
WITH RJ assembly
NO RJ assembly

## Slide 60: HDL Communications Block Diagram

## Slide 61: HDL Comms Block Detail Diagram

## Slide 62: Avionics Protocol Summary 1
Point to point protocols:
  Aurora8B10B – open standard developed by Xilinx available for implementation by anyone. We have used extensively and is a very robust point-to-point interface with fast recovery. Can be run over copper or fiber.
  Interlaken – open specification implemented in some Xilinx FPGAs. Channelized chip-to-chip.
Bus protocols:
  CAN – not suitable for strategic rad hard environments and lacks necessary bandwidth. Special physical layer transceiver.
  1553 – low bandwidth with high protocol overhead. Bulky transformers. Greater number of nodes = less bandwidth for everyone.
  EtherCat – uses Ethernet physical layer with ethernet MAC. MAC has customization. Messages pass through each system daisy chained.
Other
  SpaceFibre – Builds on SpaceWire and physical layer is fiber. IP available for licensing.

## Slide 63: Avionics Protocol Summary 2
Ethernet Technologies:
  Vanilla switched Ethernet at 1,10 gigabit. Present in every computer. Hardware is inexpensive. Can be run over Fiber or Copper
  TTE – Proprietary protocol that uses Ethernet. Company will not share source code. Used on Dream Chaser
  Time Sensitive Networking (TSN) – New IEEE standard that combines VLANS, QoS and PTP for deterministic Ethernet. Requires specialized switches and hardware
  ARINC 664 – Customization used for aircraft Ethernet Fly-by-wire. Requires specialized hardware and firmware
Ethernet Support Protocols:
  DDS – Publish/Subscribe. DDS Cert has undergone DO-178C, IEC 61508, IEC 60601/IEC 62304, and ISO 26262 certification. All code provided.
  LCM – Lightweight Control and Marshalling Protocol. Developed by MIT for low latency, high bandwidth systems
  SNMP – Simple Network Management Protocol – Could be used for asynchronous messages indicating a problem/degradation of the system
“Something like DDS or LCM is a super good idea for Guidance” – John Lupien

## Slide 64: Fiber Optic Transceiver
Processor
(GradSOC)
1000BaseX RX
1000BaseX TX
Equivalent to Small Factor Pluggable (SFP) network interface module
Risk areas associated with Fiber Optics:
Radiation Hardness of transceiver
Turn on time of transceiver after PFI
Mechanical integrity of missile environment. (shock/vibe, cleanliness)

## Slide 65: COTS Space Rad Hard Transceiver
Meet Requirements
May Meet Requirements
Further Evaluation Required
Does Not Meet Requirements
Model | Vendor | Rad | Vib | Circumvention Time | Commercial Maturity | Form Factor | Optical Specs | Data Rate | Power Monitoring
FireHawk | Samtec |  |  | <1.2ms |  | Quad XCVRPCB Mount | 850, MMF | 1/10Gbps | Yes, SPI
AVMM2 | AirBorn* |  |  | 100ms |  | Quad XCVR Active Cable Assemby | 850, MMF | 1-10Gps/per channel | Yes, I2C
All transceivers require additional test data for Dose Rate. Radiation tests reviewed by Bill Schmitt
Startup/Recovery time is long in AirBorn transceiver due to Average Power Control (APC) control loop. Operate Through?
Samtec did not have thorough radiation test reports like . Unsure if Samtec will meet Neutron requirement.
Detailed data regarding test radiation, vibration and environment are available online. Full reports will be available pending NDA
Airborn published Burn-in results (MIL-STD-883): 240 hours minimum at 125C
Notes: Provide details in same sequential order for each technology.

## Slide 66: COTS Fiber
Name | Vendor | Radiation induced attenuation -RIA (db/100m) | Fiber Type | Commercial Maturity | Core Attenuation (db/Km)
GR-50/125-23HTA | Coherent* | "Radiation-hard" | MMF |  | 3.5@850nm 1.2@1300nm
RadHard 50µm BendBright | Prysmian Group | 7.5 @ 1300nm** | MMF |  | 2.5@850nm 0.7@1300nm
Super RadHard | Prysmian Group | 4.7@ 850nm*** 2.2@ 1300nm | MMF |  | 2.6@850nm 0.6@1300nm
*IFOG Rad tests available for Single mode Coherent fiber
** Corning and Draka ( part of Prysimian Group now) on Navy Shipboard recommended Fiber optic list
** Dose 10kGy, Dose Rate 1.67Gy/s, Temperature 28C
*** Dose 2MGy, Dose Rate 1.25Gy/s, Temperature 45C
Meet Requirements
May Meet Requirements
Further Evaluation Required
Does Not Meet Requirements
Corning and Prysmian found on Navy Shipboard Fiber Optic List. Coherent fiber used in IFOG
Need actual data from manufacturers
Notes: Provide details in same sequential order for each technology.

## Slide 67: COTS Optical Connectors
*MT ferrule
** Rugged small factor utilizing MT optic ferrules , 500 mating cycles
*** Used for tactical applications
ALL PARTS bellowed SPACE Hard according to vendor
Name | Type | Vendor | Vibe | Commercial Maturity | Insertion Loss | Mating Cycles
MT Ferule Fiber Optic | High-density MT ferrule in MIL-DTL-38999 connector | Glenair* | MIL-STD-1678-3 |  | 0.5 dB (50/125) 0.3 dB (9/125) | 500 per TIA-455-21A
183-003 Series 79 MT | High-density MT ferrule in series 79 rectangular connector | Glenair** | MIL-STD-202, MIL-STD-833E |  | 0.31 dB (850 nm) 0.38 dB (1300 nm) | 500
180-132 GFR | Glenair front release in D38999 connector | Glenair*** | No public info |  | < 0.5 dB | No public info
JBDL262ABFAZ-OL-MIL | Circular expanded beam connector MIL-DTL-83526 | Fibreco | MIL-DTL-83526/20 /21 |  | 1 dB | 3000
1900Elio / ABS1696 | Rectangular Elio Socket, 7 optical termini slot | Amphenol | 3 kHz, 20 g, 12 hours |  | Less than 0.3 | 500
Meet Requirements
May Meet Requirements
Further Evaluation Required
Does Not Meet Requirements
Final connector choices will depend on mating cycles and overall link budget margin
Connectors will need to be tested for high shock experienced during stage separation
Notes: Provide details in same sequential order for each technology.

## Slide 68: Fiber Optic Testing

## Slide 69: Setup for Testing FireHawk Samtec Optical Transceiver

## Slide 70: Xilinx iBert
Using the Xilinx built-in iBert we can run PRBS-7,23,31 for days or weeks on end and check for any single error.
  Already ran fiber optic transceiver for 6 hours with no errors reported. I suspect I could run for a week with no errors. Will test.
Xilinx iBert allows direct control of electrical transceiver to adjust pre-emphasis, equalization, voltage output levels.
Can be run with optical in loopback with characteristic cable loss specs
Can be run in a vibration environment
Provides electrical margin review

## Slide 71: Measurements on FireHawk Samtec Optical Transceiver

## Slide 72: Measurements of Samtec Firehawk Optical Transceiver (Jitter Analysis)
Samtec Measured TJ = 60.4 ps
1000 BaseSX- TJ : 192ps

## Slide 73: Setup for Testing FPGA BERT implementation

## Slide 74: Measurements on FireHawk Samtec Optical Transceiver (FPGA BERT implementation)

## Slide 75: Measurements on FireHawk Samtec Optical Transceiver (Jitter Analysis)- FPGA BERT implementation
Samtec TJ = 42.26 ps Only AWG TJ= 29.91 ps

## Slide 76: Setup for Baseline Testing

## Slide 77: Middleware Timing Measurements

## Slide 78: DDS Testing Measurements
  Current test setup:
    Using RTI’s latency test
      Measures round-trip time between a publisher and subscriber
      Publisher sends packets, Subscriber echoes them
      Publisher calculates average round-trip time over 100000 packets for each of 9 sizes
    Linux-based Laptop host running Latency Publisher
    ZCU-102 running FreeRTOS and LWIP running Latency Subscriber
    Communicating over fiber ethernet
  Using RTI Connext DDS Micro 2.4.14 for testing purposes
    This version is the basis of RTI Connext DDS Cert.
    Connext DDS Cert has undergone DO-178C, IEC 61508, IEC 60601/IEC 62304, and ISO 26262 certification.
  Subscriber running on ZCU-102 has been instrumented
    Added GPIO output to break down “user-space” processing versus time used by DDS
Laptop
ZCU-102
Scope
Latency
Subscriber
Latency
Publisher
Fiber
Ethernet
Switch
GPIO

## Slide 79: DDS Testing Measurements
  Timing outputs based on GPIO Pin 0
    Output set HIGH when an ethernet packet is received.
    Output set LOW at the beginning of ‘user-space’ processing
    Output set HIGH when DDS send function called
    Output set LOW after packet send complete.
Chart: Time (us)
DDS Rx Processing
DDS Tx Processing
Application Processing

## Slide 80: DDS Timing Measurements
Packet Size (bytes) | DDS Rx Time (us) | Proc Time (us) | DDS Tx Time (us) | Total Sub Time (us)
16 | 22.27 | 6.30 | 24.63 | 53.20
32 | 22.36 | 6.40 | 24.70 | 53.46
64 | 22.30 | 6.40 | 24.60 | 53.30
128 | 22.40 | 6.44 | 24.92 | 53.76
256 | 22.54 | 6.54 | 24.88 | 53.96
512 | 22.52 | 6.74 | 24.84 | 54.10
1024 | 24.00 | 6.93 | 25.33 | 56.27
2048 | 23.34 | 7.50 | 31.26 | 62.10
4096 | 24.16 | 8.51 | 35.24 | 67.91
DDS Reported latency is latency reported by the Publisher on Linux Laptop after processing
Numbers are very stable & repeatable on ZCU-102
Performance with Publisher on a ZCU-102 is expected to be similar to Subscriber
  Comms on publisher are essentially doing the same thing as subscriber
Chart: Packet Size
| 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
DDS Rx | 22.27 | 22.36 | 22.3 | 22.4 | 22.54 | 22.52 | 24 | 23.34 | 24.16
Processing | 6.3 | 6.4 | 6.4 | 6.44 | 6.54 | 6.74 | 6.93 | 7.5 | 8.51
DDS Tx | 24.63 | 24.7 | 24.6 | 24.92 | 24.88 | 24.84 | 25.33 | 31.26 | 35.24

## Slide 81: Demo Setup
Test of all internal and external comms working simultaneously
Simulated Data based on LE

## Slide 82: Backup

## Slide 83: Avionics Network Systems Approach Highlights
Managed Systems Communication Approach
Tactical Timelines
Coordination, Interface and Data
Rad Hard and Circumvention and Recovery
Test Integration
SWS MBE Virtual Environment Simulation
Cyber Authentication and Test Analysis

## Slide 84
DETERMINISTIC
NON-DETERMINISTIC
ADVANTAGES:
Easier reproduction of errors for development and fleet support
Defined set of V&V test vectors
Flexibility for technology upgrades, reallocation, or future node insertions
Consistent Network Communications rules throughout
distributed system
DISADVANTAGES:
Communications structure and rules need to be established
ADVANTAGES:
Application transparent to communications infrastructure
Simple use on demand protocol
DISADVANTAGES:
Poor reproducibility of errors
Requires coordination between applications to minimize effects of system bottlenecks
Infinite set of V&V test vectors
Application Designers would each implement their own API and would establish their own intercommunication standards (much like current COORD)
Deterministic timing is a function of performance capabilities of system
Poorly defines structure for mapping application
Possible detailed analysis required for new technology or application reallocation
A Deterministic Approach to Communications Provides a
Strong Scalable Structure for LE2 Design and Future Enhancements
Managed Systems Communication Approach

## Slide 85: Tactical Timelines
Initial numbers indicate less than 10% for all tactical timelines
Chart: Packet Size (bytes) vs Time to Process (us)
| 100 | 500 | 1000 | 1400
F2R | 6.8386 | 6.8942 | 6.8392 | 6.8942
Phy Recv | 1.33 | 1.28 | 1.33 | 1.39
PBUF to DDR4 | 0.834 | 1.112 | 1.279 | 1.39
DD4 to BRAM | 3.78 | 4.56 | 5.28 | 6.28
BRAM 2 DDR4 | 3.725 | 4.23 | 4.78 | 5.28
UDP Send | 3.45 | 3.75 | 3.95 | 4.28

## Slide 86: Rad Hard & Circumvention and Recovery (C&R)
Hardware Transceiver and PHY implemented in Processor will require testing
Guidance is master of communications, modes, and states to RBs and Flight Control
If Flight Control is integrated with guidance, then C&R is handled intrinsically
If Flight Control is external to guidance, then some independent discrete may be needed
RBs may need independent discrete to indicate C&R (TBD)
Current Indications are that boot time of comms hardware, processor, and stack will support the 3ms recovery time.
Current FCEA Timeline

## Slide 87: Cyber Authentication and Test
Authentication for all network nodes
Network will allow for addition/subtraction of authorized test equipment and data display
Constant network monitoring for intrusion of not allowed network devices connected to network
Monitoring and logging of general health and welfare of the network
Test data logging to support to quick cyber response verification